## Slide 1: (K－, K＋)反応用新規磁気スペクトロメータの設計と現状 Design and Status of S-2S
金築俊輔 （京大理）
S. Kanatsuki (Kyoto University)
「ストレンジネスを含む原子核の最近の展開」研究会@熱川
2014.9.26

## Slide 2: Outline
(K－,K＋) reaction
Plan of J-PARC E05
S-2S spectrometer
  Magnets
    Field measurements, calculation
  Detectors
    Resolutions
    Backgrounds
Timeline
Summary
2014.9.26

## Slide 3: Doorway to Strangeness -2
K－p Ξ－K＋
研究会「ストレンジネスを含む原子核の最近の展開」
2014.9.26
C.B. Dover and A. Gal, Ann. Phys. 146, 309 (1983)
Elementary process
〜35 ub/sr around 1.8 GeV/c

## Slide 4: Kinematics
研究会「ストレンジネスを含む原子核の最近の展開」
2014.9.26
pK＋ = 1.2～1.4 GeV/c
Recoil Momentum
Momentum of K＋
pK－ = 1.8 GeV/c

## Slide 5: Missing Mass Resolution
p’B 1×10－3 | 1.67 |  |  | 1.8
p'S 3×10－3 |  | 3.74 |  | 3.8
p’B, p’S | 1.67 | 3.74 | 0.04 | 4.1
研究会「ストレンジネスを含む原子核の最近の展開」
2014.9.26
dp/p | Beam | Scat | θ | ΔM
pB,pS 5×10－4 | 0.84 | 0.62 | 0.04 | 1.0
1 MeV  3 g/cm2
2 MeV  6 g/cm2
3 MeV  10 g/cm2
ΔEstrag  Target thickness
SKS limits ΔMM
12C(K－,K＋) Ξ12Be, θ=5°, Ehyp=0 MeV, Δθ=2mrad
[MeV]
Good!
Current B.L. Performance
SKSminus
High-Res Spec. “S-2S”

## Slide 6: J-PARC E05
研究会「ストレンジネスを含む原子核の最近の展開」
2014.9.26
Spectroscopy: 12C(K－,K＋) Ξ12Be
Spectrometers
  K－  Beam spectrometer at K1.8BL
  K＋  SKS or S-2S
K－ beam intensity
  Factors
    Main Ring power: 30 kW  100 kW ×10/3
    Primary target: Au  Ni ×1/2
    Spill cycle: 6s  4s ×3/2
    Beamline fine tuning: ×1.2
×3
SKS: Existing in K1.8Area (～2015)
S-2S: Now under construction
(T1 is always troublesome…)
100 kW  13.5×106 K－/min
30 kW  4.5×106 K－/min
    If lower momentum, pK－=1.7 GeV/c  ×0.7?

## Slide 7: Yield Estimation
研究会「ストレンジネスを含む原子核の最近の展開」
2014.9.26
Notes
  Efficiency = 0.7
  Differencial cross section  Result of the BNL-E885 (Khaustov et al.)
 | SKSminus | S-2S
Acceptance | 110 msr | 55 msr
K＋ survival rate | 0.6 | 0.4
Cross section | 42 nb/sr (θ<14deg) | 89 nb/sr (θ<8deg)
Beam intensity | 4.5×105 /6s | 9×105 /4s
Target | 9.3 g/cm2 CH2 | 3 g/cm2 12C
Yield [/month] | 140 events | 110 events

## Slide 8
研究会「ストレンジネスを含む原子核の最近の展開」
2014.9.26
S-2S spectrometer

## Slide 9: S-2S spectrometer
研究会「ストレンジネスを含む原子核の最近の展開」
2014.9.26
New spectrometer for K＋
  Construction has started since 2012
Requirement
  1.2～1.4 GeV/c
  dp/p ～5×10－4 (FWHM)
K1.8 area
  Narrow space
  Available power supply
Target
K－
K＋

## Slide 10: Configuration
研究会「ストレンジネスを含む原子核の最近の展開」
2014.9.26
Trigger counters
Momentum reconstruction
Path Length ～9 m
K＋: survival rate 40%

## Slide 11: Magnets
研究会「ストレンジネスを含む原子核の最近の展開」
2014.9.26
Three normal conducting magnets
Q1,D1  Newly constructed
Q2  Modification of pole and coil from old magnet
Q1
Q2
D1
Horizontal focus
～8.5 m @1.37GeV/c
1.37GeV/c±7.5%

## Slide 12: Acceptance
研究会「ストレンジネスを含む原子核の最近の展開」
2014.9.26
Magnetic field  TOSCA calculation
Q1,Q2,D1 = 2500A (max)
4°
8°
p=1.35 GeV/c
T2-Q1=55cm
～55 msr
Particles just passing through the magnets
= not including detector configuration
18°

## Slide 13: Momentum Resolution
研究会「ストレンジネスを含む原子核の最近の展開」
2014.9.26
Momentum [GeV/c]
Position resolution (rms) [um]
w/ Multiple Scattering
position resolution only
Momentum resolution
Momentum resolution
dp/p [×104]
dp/p [×104]
p = 1.375 GeV/c
dp/p 5～6×10－4 (FWHM)
Magnet condition
Q1,Q2,D1 = 2500A (max)
σx = 250um (rms)

## Slide 14: Magnets
研究会「ストレンジネスを含む原子核の最近の展開」
2014.9.26

## Slide 15: Q1 magnet
研究会「ストレンジネスを含む原子核の最近の展開」
2014.9.26
Vertical focus
2.4×2.4×0.88 m3
Aperture 31 cm
Total weight 37 ton
8.7 T/m
Completed 2013.3
Painted
Build up

## Slide 16: Field Measurement
研究会「ストレンジネスを含む原子核の最近の展開」
2014.9.26
Excitation curves (at center)
Distributions (500,2000,2500 A)
Hall probe
8.7 T/m

## Slide 17: Field Calculation
研究会「ストレンジネスを含む原子核の最近の展開」
2014.9.26
3D electromagnetic analysis with Opera-3d/TOSCA
BHcurve adjustment
Measurement
Calculation
Residual
±20 Gauss

## Slide 18: Q2 magnet
研究会「ストレンジネスを含む原子核の最近の展開」
2014.9.26
Horizontal focus
2.1×1.54×0.5 m3
Aperture 36 cm
Total weight 12 ton
5.0 T/m (measurement)
Pole Cut
Coil modification
Completed in 2014.3

## Slide 19: D1 magnet
研究会「ストレンジネスを含む原子核の最近の展開」
2014.9.26
1.5 T = 70 deg. bend @1.37 GeV/c
Pole length 3.67 m
Gap 80×32 cm2
Weight 86 ton
Painted
2014.3
Magnets in KEK

## Slide 20: D1 magnet
研究会「ストレンジネスを含む原子核の最近の展開」
2014.9.26
Calculation by Opera-3d/TOSCA
1.49 Tesla
20~50 Gauss @Counters

## Slide 21: Detectors
研究会「ストレンジネスを含む原子核の最近の展開」
2014.9.26

## Slide 22: Tracking Detectors
研究会「ストレンジネスを含む原子核の最近の展開」
2014.9.26
4 sets: entrance=SDC1,2, exit=SDC3,4
Required size
  15W×28H cm2 at SDC2
  90W×50H cm2 at SDC4
Future works
  Existing = SDC1,3,4
  SDC3,4  Repairment
  SDC2  New
Old SKS SDC3 in KEK
1×1 m2 drift chambers

## Slide 23: Trigger Counters
研究会「ストレンジネスを含む原子核の最近の展開」
2014.9.26
Backgrounds
  π＋, p : 1000
  K＋ : 1
K＋ = TOF ∧ AC ∧ WC
K+ Trigger
Cherenkov counters
Proton veto
Water: n=1.33
(Talk by Takenaka)
Pion veto
Aerogel: n=1.06
Offline PID
Plastic Scintillator
(Beam = 106 K−)
Roughly estimated from previous
experiment at BNL, KEK
pion
kaon
proton

## Slide 24: Backgrounds
研究会「ストレンジネスを含む原子核の最近の展開」
2014.9.26
2. Decay of beam K－
  K－  π－π－π＋ (B.R. 5.6%)
  K－@1.8 GeV/c: βγcτ 〜13.5 m
3. Reactions on the D1 yoke
  K－ + Fe  many particles
1. Various products off targets
  Reaction rate: ～10%
“D1Hit event”
3 m

## Slide 25: Backgrounds not from the Target
研究会「ストレンジネスを含む原子核の最近の展開」
2014.9.26
Decay of beam K－ & Reactions on the D1yoke
a few tens of π＋ from K− decay
Only neutrons can reach the counters at the exit
Most charged particles stop inside of the D1
Particles passing through the magnets
Geant4 simulation
Beam K− =106

## Slide 26: Reactions in target
研究会「ストレンジネスを含む原子核の最近の展開」
2014.9.26
12C
K－p  Ξ－K＋
K－p  Ξ*－ K＋
K+
K－
p
K－p  p K－
K－p  p πK
K－n  p π－K－
Decay of hyperons
π+
K－p  Λπ＋π－
K－p  Σ－π＋
Background estimation
  JAM v1.210 : Jet AA Microscopic transport model
Y. Nara et.al., Phys. Rev. C61 (2000) 024901
S-2S: θ＜18°
1.2~1.4 GeV/c
Out of Acceptance!
  “Compilation of Cross-Sections : K± induced reactions”, CERN-Library(1983)

## Slide 27: Background Distributions
+DetectorCut
研究会「ストレンジネスを含む原子核の最近の展開」
2014.9.26
JAM simulation
106K－@1.8GeV/c
3 g/cm2, 12C target
Λ
Σ－

## Slide 28: Timeline
研究会「ストレンジネスを含む原子核の最近の展開」
2014.9.26
Magnet
Drift Chamber
Trigger Counters
Q1,Q2
D1
SDC1
TOF
AC
WC
SDC2
SDC3,4
Completed (’13/’14)
Yoke only
Ready
Almost ready
Materials are ready
Ready
Prototypes
Test experiments
@J-PARC&ELPH
Magnet Table
Coil Mount
2014.9
2015.4
Design of support frame
Performance check
Design
Production
Performance check
Design actual version
Field measurement
/calculation
Design/production PreAmpBoard
Repairment on some parts/check
Fabrication
Performance check
Setup
Others: HeBag
Ready for installation in JFY2015

## Slide 29: Summary
研究会「ストレンジネスを含む原子核の最近の展開」
2014.9.26
Ξ-hypernuclear spectroscopy (J-PARC E05)
  Phase0: with SKS  medium resolution
  Phase1: with S-2S  high resolution
Construction of S-2S is in progress
  Performance
    dp/p ＜ 6×10－4
    dΩ 55 msr
  Magnets
    Q1 and Q2 are completed.
    D1 will be completed in JFY2014
  Detectors
    Many materials are ready.
    1DC, WC will be newly fabricated.
(1.3～1.4 GeV/c)