## Slide 1
Shunsuke Kanatsuki for the E492 collaboration
Kyoto University
2016/8/24
E492
Test of a Scintillating Fiber Target for the Hypernuclear Spectroscopy

## Slide 2: Outline
Motivation
  Spectroscopy of hypernuclei at J-PARC
  Active fiber target
Experiment at RCNP
  Purpose : study response of a fiber using proton beam
  Setup
  Run time estimation : 2 days including beam tuning.
Summary

## Slide 3: Physics Motivation
Hypernuclear spectroscopy
  Baryon-baryon interaction nuclear force
  A role of strangeness in dense nuclear matter
Neutron stars
S=-∞
F. Weber, PPNP 54(2005)193
neutron star core
extended

## Slide 4: Spectroscopy at J-PARC K1.8BL
Scat. K+
~1.3 GeV/c
J-PARC E05
  Missing-mass spectroscopy of Ξ-hypernucleus, using the 12C(K−, K+)12ΞBe reaction (Nagae et al.)
observe peak structures of the bound states
   deduce the information of ΞN interaction
Approved as highest priority “Day-1 experiment”
Momentum analysis
K+ : S-2S spectrometer
  magnet construction completed in 2015
  will be installed to J-PARC in 2018
K− : Beam spectrometer
Missing-mass resolution ΔM
1-1.8 MeVFWHM w/o energy loss straggling in the target (Estrag)
Our goal: ΔM＜2 MeV
Estrag＜0.8 MeV
D1
Q2
Q1
SDC1,2
WC
AC
TOF
SDC3,4
Beam K−
1.8 GeV/c
Target

## Slide 5: Expected Spectrum
DWIA calculation
  12C (K－,K＋)Ξ12Be at 1.8 GeV/c
  Core nucleus excitation is taken into account
T. Motoba and S. Sugimoto, Nucl. Phys. A 835, 223 (2010)
Need ΔM ＜2 MeV

## Slide 6: Production Rate
  K− beam intensity = 0.6MHz
  *BNL-E885 exp. : P. Khaustov, et al., PRC 60, 054603 (2000)
Target thickness
  10 g/cm2 is desirable to achieve good statistics within reasonable run time at J-PARC
   Estrag. ＞4 MeVFWHM
  Direct measurement of the energy loss event-by-event
  to achive both high mass resolution and statistics
 | Cross section | Yield [/4weeks /1g/cm2]
12ΞBe | 89±14 nb/sr* | 37 counts

## Slide 7: Active Fiber Target
Scintillating fiber
  scintillation light yield  correction of the energy of kaons event-by-event
K+
K−
12ΞBe
Target volume

## Slide 8: Active Fiber Target
Scintillating fiber
  scintillation light yield  correction of the energy of kaons event-by-event
K+
K−
Λ
Λ
π0
n
p
π−
Target volume

## Slide 9: Active Fiber Target
Energy losses of
Beam K−
Scat. K+
Decay particles from hypernucleus
should be measured separately  Target must be segmented
 Use fibers
Scintillating fiber
  scintillation light yield  correction of the energy of kaons event-by-event
K+
K−
Λ
Λ
π0
n
p
π−
Target volume
12ΞBe

## Slide 10: Active Fiber Target
Scintillating fiber bundle
  3x3 mm square or 3 mm Φ ( 50×18+16×18 ≒ 1000)
  MPPCs attached on the both ends of each fiber
10.8 cm
15 cm
5 cm

## Slide 11: Performance Test at RCNP
Measurement with a single fiber
  study the correlation between
    the energy loss Grand Raiden
    light yield Scintillating Fiber
proton
E1
E2
Eloss = E1ーE2
fiber
MPPC  ADC  NPEs
Grand Raiden
Target system
scintillation
measured with
The whole performance of the target (fiber bundle)
 estimate by simulation using the response of a single fiber

## Slide 12: Experimental Setup
Beam
  WS beam line
  proton at 392 MeV
    Eloss should be close to that of kaons
  intensity: 5 kHz
Grand Raiden
  0 degree
  Eloss resolution 30 keV
    need dispersion matching condition
High-resolution measurement with high velocity particle
feasible only in RCNP with the Grand Raiden
700keV
1270keV
160keV
FWHM
240keVFWHM
proton @392 MeV
β=0.709
Eloss distribution
K− @1.8 GeV/c
β=0.964
3mm-thick fiber

## Slide 13: Experimental Setup
Au
ZnS
Empty
Fiber
14 cm
Schematic of target ladder
MPPC
MPPC
Bias
Signal
LED
LED
beam
Fiber
  fixed by a target ladder in the scattering chamber
  specification
    cross-section: 3x3mm2 square, 3mmΦ
    crad: single, double
    company: KURARAY, SAINT-GOBAIN
      candidates narrowed down in advance
Target ladder
  will be newly fabricated
  hold a fiber and
    Au foil : beam & spectrometer tuning
    ZnS : beam profile check
    Empty : beam energy check

## Slide 14: Run time estimation
Beam tuning and spectrometer start-up：1 day
  start up the spectrometer
  tuning the accelerator
  optimization the dispersion matching condition
Fiber test : 2 hours ×12 conditions = 1 day
  Conditions
    3 kinds of fibers × 4 (for check the individual difference)
  Setup change : 1.5 hour
    replace a fiber with chamber open
  Beam irradiation : 0.5 hour
    ZnS, Empty : beam check
    Fiber : energy loss measurement

## Slide 15: Summary
We propose a performance test of a scintillating fiber using proton beam at 392 MeV at WS course.
  Feasible only at RCNP with Grand Raiden
The responses of fibers for the energy loss of proton beams are studied.
  correlation between light yield in fiber and the energy loss measured by Grand Raiden
The study is very important for the Ξ hypernuclear spectroscopy at J-PARC.
  to optimize the mass resolution and statistics
  will be carried out in FY2018 in the earliest case.
  We request beam time for this test in FY2017

## Slide 16: Collaboration List
Kyoto University
  H. Fujioka, T. Furuno, S. Kanatsuki, T. Kawabata, M. Murata, T. Nagae, T. Nanamura, A. Sakaue
Osaka University, RCNP
  T. Gogami, A. Inoue, N. Kobayashi, A. Tamii
JAEA, ASRC
  Y. Ichikawa

## Slide 17: Back up

## Slide 19: Energy Loss Distribution
Geant4 simulation
Sum of the energy losses in the whole target
Target system : xx’yy’ ×9 sets = 36 layers
Thickness：10.8 cm = 11.23 g/cm2 (Carbon fraction: 10.4 g/cm2)
Beam: K− 1.8 GeV/c, position: uniform, direction: 0 degree
MPV: 24.17 [MeV]
FWHM:5.73 [MeV]
MPV: 30.43 [MeV]
FWHM: 4.11 [MeV]
Square type
Round type

## Slide 20: Incident Position Dependence
3mmΦ Round type fiber
Energy loss of proton at 392 MeV
Pencil beam : incident position fixed at center
Broad beam : incident position uniform
  distribution includes position dependence
Energy loss [MeV]
1220keV
1270keV
350keVFWHM
240keVFWHM
Incident position [cm]
Energy loss [MeV]

## Slide 21: Energy Loss in Crad
Simulation condition
  3mmΦ Round type fiber
  Energy loss of proton at 392 MeV
  Broad beam : incident position uniform
Eloss(all) − Eloss(core)
Eloss (all) [MeV]
Eloss(all) − Eloss(core)
Eloss (core) [MeV]
Correlation

## Slide 22: Beta and Eloss
particle | beta | Energy loss (MPV) [MeV] | ΔE (FWHM) [MeV]
1.8 GeV/c K- | 0.964 | 0.701 | 0.16
1.3 GeV/c K+ | 0.935 | 0.745 | 0.18
392 MeV proton | 0.709 | 1.267 | 0.24
350 MeV proton | 0.685 | 1.370 | 0.29
300 MeV proton | 0.653 | 1.500 | 0.32
250 MeV proton | 0.614 | 2.098 | 0.48
200 MeV proton | 0.566 | 2.355 | 0.62

## Slide 23: Readout
EASIROC
signal
RCNP DAQ
DAQPC
(Ethernet)
Focal plane
Trigger circuit
EASIROC: Multi-channel Readout Module
Notes: ・Easirocの最大shaping timeである175ns以内にトリガーを入れる必要あり
(8m程度のケーブルによる減衰は許容できるので、EASIROCモジュールはトリガー生成回路の近くに設置できる)
・Easirocでの読み出しとRCNPDAQをどう合わせるかは要検討

## Slide 24: Event-by-event correction
Simulation of 10g/cm-thick fiber bundles
Correction using total Eloss without distinguish the decay particle result in making long and large tail in the low mass side.
w/o decay
decay contamination

## Slide 25: Energy Resolution
Assumption
  Case 1: good spectrometer resolution (dp/p = 5×10-4 for both Beam and S-2S)
  Case 2: current performance of beam spectrometer (dp/p = 1×10-3)
ΔEstrag. should be ＜0.8 MeVFWHM in case 2 for ΔM＜2 MeVFWHM
 | Beam | Scat | θ | ΔM
Case 1 | 0.84 | 0.62 | 0.04 | 1.0
Case 2 | 1.67 |  |  | 
 |  |  |  | 1.8
Scat. K+
Beam K−
Missing-mass Resolution
Energy loss
straggling
Angular
unit : MeV

## Slide 26: Expected Spectra
T. Motoba and S. Sugimoto, Nucl. Phys. A 835, 223 (2010)
ΔEexp = 1.5 MeV
ΔEexp = 3 MeV
16O (K－,K＋) ΛΛ16C
T. Harada et al., Phys. Lett. B 690, 363 (2010)
12C (K－,K＋)Ξ12Be
Need 2 MeV
or further better ΔM
J-PARC and
new spectrometer

## Slide 27: Production Rate
  K− intensity = 1M/4s, (Acc. Power ~80kW in 2018?)
  ref1. BNL-E885 exp. : P. Khaustov, et al., PRC 60, 054603 (2000),
  ref2. T. Harada, et al., PLB 690, 363 (2010)
Target thickness
  ＞10 g/cm2 is desirable to achieve good statistics within reasonable run time at J-PARC
   Energy loss straggling ＞4 MeVFWHM
   Can’t perform high-resolution spectroscopy
 | Cross section | Yield [/4weeks /1g/cm2]
12ΞBe | 89±14 nb/sr (ref.1) | 37 counts
12ΛΛBe | 5-7 nb/sr (ref.2) | 3 counts

## Slide 28: Scintillating Fiber and MPPC
Fiber: Material
Core: Polystyrene(CH) (1.05 g/cm3)
Cladding: Acrylic (1.18 g/cm3)
Clad thickness T: 2％ of fiber size
T
T
MPPC
ねじで治具と固定
治具
fiber hold
MPPC
HAMAMATSU S13360-3075PE
Photosensitive area: 3mm×3mm
Gain 1.7×106
Air contact to fiber

## Slide 29: Eloss in Crad (all)
Simulation for 36 layers
Eloss(all) – Eloss(core)
long tail
Round type
Square type

## Slide 30: Energy loss in 1 fiber

## Slide 31: Energy loss in 1 fiber

## Slide 32: Position Dependence
中心だけに当てた時との比較
位置依存性
Path length [mm]
Incident position [mm]

## Slide 33: クラッドの効果の位置依存性(p)
Energy loss – Energy deposit
(Energy loss – Energy deposit) /Energy loss